## Slide 1: Linux device driver
Day 35 PPT
-SUBITHRA s

## Slide 2
lseek is a system call in Unix and Unix-like operating systems that changes the current position (offset) of a file descriptor. Here’s a simplified explanation:
Purpose
lseek is used to move the file pointer to a specific location within an open file, allowing for random access (i.e., reading or writing at any position within the file).
off_t lseek(int fd, off_t offset, int whence);
lseek

## Slide 3
Parameters
fd: The file descriptor of the file.
offset: The position to move the file pointer to.
whence: The reference point for the offset. It can be:
SEEK_SET: From the beginning of the file.
SEEK_CUR: From the current position.
SEEK_END: From the end of the file.
Return Value
On success: Returns the new offset.
On failure: Returns -1 and sets errno.
Use Cases
Move to the beginning of a file: lseek(fd, 0, SEEK_SET).
Skip ahead or back: lseek(fd, n, SEEK_CUR) (where n can be positive or negative).
Move to the end of a file: lseek(fd, 0, SEEK_END).
lseek

## Slide 4
The kernel uses a structure, often referred to as cred, to manage the credentials of a process. This structure includes several fields related to user IDs and group IDs, which help determine what permissions a process has when accessing system resources.
User IDs
User ID (UID): The unique identifier for a user on the system.
Kernel Credentials

## Slide 5
Current User ID (cuid): This term isn't standard in Unix terminology, but if referenced, it typically means the real user ID (ruid) or the saved user ID (suid), depending on the context. More commonly, Unix-like systems use:
Real User ID (ruid): The UID of the user who created the process. It identifies the actual user who owns the process.
Saved User ID (suid): Used to save the previous effective UID when a process's effective UID is changed temporarily. It allows the process to switch back to the original effective UID.
Effective User ID (euid): The UID that the kernel uses to determine the permissions of a process for most operations, such as accessing files and making system calls. It can be different from the real UID, especially when executing setuid programs.
Kernel Credentials

## Slide 6
Kernel Credentials

## Slide 7
Role of device-drivers
hardware devices
network
device driver
Linux
operating system
kernel
networking
subsystem
application
program
standard
runtime
libraries
user space kernel space
file
subsystem
character
device driver

## Slide 8
Source-code layout
#include <linux/module.h>
#include <linux/etherdevice.h>
…
typedef struct {
/* driver’s private data */
} MY_DRIVERDATA;
char modname[ ] = “netframe”;
struct net_device *netdev;
netframe.c
my_init
my_exit
The mandatory module-
administration functions
my_open()
my_stop()
my_hard_start_xmit()
my_isr()
my_get_info()
The network driver’s
“payload” functions
Optional pseudo-file (for
debugging assistance)

## Slide 9: Interactions with the kernel
module_init() calls ‘register_netdev()’
module_exit() calls ‘unregister_netdev()’
open() calls ‘netif_start_queue()’
stop() calls ‘netif_stop_queue()’
hard_start_xmit() calls ‘dev_kfree_skb()’
rx_handler() calls ‘dev_alloc_skb()’ and netif_rx()’

## Slide 10: ‘mynetdvr.c’
We can demonstrate the basic transmit and receive functionality of our network driver using a pair of ‘anchor’ machines
But we have to work around some slight amount of interference with the already-installed ‘e1000’ network-driver which is supporting our ability to do remote login via the ‘eth0’ device interface

## Slide 11: Building Blocks
Nodes: PC, special-purpose hardware…
  hosts
  switches
Links: coax cable, optical fiber…
  point-to-point
  multiple access
■ ■ ■
(a)
(b)

## Slide 12: Switched Networks
  two or more nodes connected by a link, or
  two or more networks connected by a node
A network can be defined recursively as...

## Slide 13: Firewall configurations

## Slide 14: Addressing and Routing
Address: byte-string that identifies a node
  usually unique
Routing: process of forwarding messages to the destination node based on its address
Types of addresses
  unicast: node-specific
  broadcast: all nodes on the network
  multicast: some subset of nodes on the network

## Slide 15: Inter-Process Communication
Turn host-to-host connectivity into process-to-process communication.
Fill gap between what applications expect and what the underlying technology provides.

## Slide 16: Multiplexing
Circuit switching: carry bit streams
  original telephone network
Packet switching: store-and-forward messages
  Internet

## Slide 17: Statistical Multiplexing
On-demand time-division
Schedule link on a per-packet basis
Packets from different sources interleaved on link
Buffer packets that are contending for the link
Buffer (queue) overflow is called congestion
■ ■ ■

## Slide 18: Conceptual layering of protocol software
Layer n
Layer 2
Layer 1
Message sent
Message received
Communication
medium
Sender
Recipient

## Slide 19: Encapsulation as it is applied in layered protocols

## Slide 20: ISO Architecture

## Slide 21: OSI protocol summary
Layer
Description
Examples
Application
Protocols that are designed to meet the communication requirements of
specific applications, often defining the interface to a service.
HTTP,
FTP
,
SMTP,
CORBA IIOP
Presentation
Protocols at this level transmit data in a network representation that is
independent of the representations used in individual computers, which may
differ. Encryption is also performed in this layer, if required.
Secure Sockets
(
SSL),CORBA Data
Rep.
Session
At this level reliability and adaptation are performed, such as detection of
failures and automatic recovery.
Transport
This is the lowest level at which messages (rather than packets) are handled.
Messages are addressed to communication ports attached to processes,
Protocols in this layer may be connection-oriented or connectionless.
TCP,
UDP
Network
Transfers data packets between computers in a specific network. In a WAN
or an internetwork this involves the generation of a route passing through
routers. In a single LAN no routing is required.
IP,
ATM virtual
circuits
Data link
Responsible for transmission of packets between nodes that are directly
connected by a physical link. In a WAN transmission is between pairs of
routers or between routers and hosts. In a LAN it is between any pair of hosts.
Ethernet MAC,
ATM cell transfer,
PPP
Physical
The circuits and hardware that drive the network. It transmits sequences of
binary data by analogue signalling, using amplitude or frequency modulation
of electrical signals (on cable circuits), light signals (on fibre optic circuits)
or other electromagnetic signals (on radio and microwave circuits).
Ethernet base- band
signalling,
ISDN

## Slide 22: TCP/IP layers
Messages (UDP) or Streams (TCP)
Application
Transport
Internet
UDP or TCP packets
IP datagrams
Network-specific frames
Message
Layers
Underlying network
Network interface

## Slide 23: Encapsulation in a message transmitted via TCP over an Ethernet
Application message
TCP header
IP header
Ethernet header
Ethernet frame
port
TCP
IP

## Slide 24: Protocol Multiplexing
Multiplexing and Demultiplexing (demux key)
Encapsulation (header/body)
Host
Host
Application
program
Application
program
RRP
Data
Data
HHP
RRP
HHP
Application
program
Application
program
RRP Data
RRP Data
HHP RRP Data

## Slide 25: Scalable Networks
Switch
  Connect links to form a larger network.
  Connect switches to form a larger network.
  forwards packets from input port to output port
  port selected based on address in packet header
Advantages
  store and forward
  support large numbers of hosts

## Slide 26: Datagram Switching
No connection setup phase
  Sometimes called connectionless model
Each packet forwarded independently
Each switch maintains a forwarding (routing) table
  Eg. Switch 1

## Slide 27: Internetworking
Concatenation of Different Networks

## Slide 28: IP Internet
Connecting Problem 1: Heterogeneity of Networks
  Solution: Layered Protocol Stack (IP over …… )
Problem 2: Scalability in Routing and Addressing
  Solution: Address Hierarchy

## Slide 29: Simple Demultiplexor (UDP)
Unreliable and unordered datagram service
Adds multiplexing
No flow control or error control
  no need for sender-side buffer)
Endpoints identified by ports
  servers listens at well-known ports!
  see /etc/services on Unix
Header format
Optional checksum
  psuedo header (IP.src, IP.dsest, IP.proto, UDP.len) + UDP header + data

## Slide 30: TCP Overview
Connection-oriented
Byte-stream
  app writes bytes
  TCP sends segments
  app reads bytes
Full duplex
Flow control: keep sender from overrunning receiver
Congestion control: keep sender from overrunning network
Application process
Write
bytes
TCP
Send buffer
Segment
Segment
Segment
Transmit segments
Application process
Read
bytes
TCP
Receive buffer
■ ■ ■

## Slide 31
THANK YOU