## Slide 1: Linux device driver
Day 32 PPT
-SUBITHRA s

## Slide 2: ioctl
Input/output control
System call
For operations beyond simple data transfers
  Eject the media
  Report error information
  Change hardware settings
  Self destruct
Alternatives
  Embedded commands in the data stream
  Driver-specific file systems

## Slide 3: ioctl
User-level interface (application view)
  Int ioctl(int fd, int request, ...);
  ...
    Does not indicate variable number of arguments
      Would be problematic for the system call interface
    In this context, it is meant to pass a single optional argument
      Traditionally a char *argp
      Just a way to bypass the type checking
  For more information, look at man page

## Slide 4: ioctl
Driver-level interface
  Int (*unlocked_ioctl) (struct file *filp,
  unsigned int cmd,
  unsigned long arg);
  Cmd is passed from the user unchanged
  Arg can be an integer or a pointer
  Compiler does not type check
Ioctl() has changed from the LDD3 era
  Modified to remove the big kernel lock (BKL)
  Http://lwn.Net/articles/119652/

## Slide 5: Choosing the ioctl Commands
Desire a numbering scheme to avoid mistakes
  E.G., Issuing a command to the wrong device (changing the baud rate of an audio device)
  Unique ioctl command numbers across system
  Check ioctl.H files in the source and directory documentation/ioctl/

## Slide 6: Choosing the ioctl Commands
A command number uses four bitfields
  Defined in include/uapi/asm-generic/ioctl.H
    (For most architectures)
  < Direction, type, number, size>
    Direction: direction of data transfer
      _IOC_NONE
      _Ioc_read
      _Ioc_write
      _Ioc_read | write

## Slide 7: Choosing the ioctl Commands
  < Direction, type, number, size>
    Type (ioctl device type)
      8-bit (_IOC_TYPEBITS) magic number
      Associated with the device
    Number
      8-bit (_IOC_NRBITS) sequential number
      Unique within device

## Slide 8: Choosing the ioctl Commands
  < Direction, type, number, size>
    Size: size of user data involved
      _Ioc_sizebits
        Usually 14 bits but could be overridden by architecture
    #Define scull_iocsquantum _iow(scull_ioc_magic, 1, int)
/* provoke compile error for invalid uses of size argument */
extern unsigned int __invalid_size_argument_for_IOC;
#define _IOC_TYPECHECK(t) \
((sizeof(t) == sizeof(t[1]) && \
sizeof(t) < (1 << _IOC_SIZEBITS)) ? \
sizeof(t) : __invalid_size_argument_for_IOC)

## Slide 9: Choosing the ioctl Commands
Useful macros to create ioctl command numbers
  _Io(type, nr)
  _Ior(type, nr, datatype)
  _Iow(type, nr, datatype)
  _Iowr(type, nr, datatype)
_IO*_BAD used for backward compatibility
  Uses number (of bytes) rather than datatype
  Http://lkml.Iu.Edu//hypermail/linux/kernel/0310.1/0019.Html

## Slide 10: Choosing the ioctl Commands
Useful macros to decode ioctl command numbers
  _IOC_DIR(nr)
  _IOC_TYPE(nr)
  _IOC_NR(nr)
  _IOC_SIZE(nr)

## Slide 11: Choosing the ioctl Commands
The scull example
/* Use 'k' as magic number (type) field */
#define SCULL_IOC_MAGIC 'k‘
/* Please use a different 8-bit number in your code */
#define SCULL_IOCRESET _IO(SCULL_IOC_MAGIC, 0)

## Slide 12
THANK YOU