## Slide 1: Block Drivers
BHAVANA
DAY 36
23/05/2024

## Slide 2: Topics
Block drivers
Registration
Block device operations
Request processing
Other details

## Slide 3: Overview of data structures

## Slide 4: Block Drivers
Provides access to devices that transfer randomly accessible data in blocks, or fixed size chunks of data (e.g., 4KB)
  Note that underlying HW uses sectors (e.g., 512B)
Bridge core memory and secondary storage
  Performance is essential
  Or the system cannot perform well
Lecture example: sbull (Simple Block Device)
  A ramdisk

## Slide 5: Block driver registration
To register a block device, call
int register_blkdev(unsigned int major,
const char *name);
  major: major device number
    If 0, kernel will allocate and return a new major number
  name: as displayed in /proc/devices
To unregister, call
int unregister_blkdev(unsigned int major,
const char *name);

## Slide 6: Disk registration
register_blkdev
  Obtains a major number
  Does not make disk drives available to the system
Need additional mechanisms to register a disk
  Need to know two data structures:
    struct block_device_operations
      Defined in <linux/blkdev.h>
    struct gendisk
      Defined in <linux/genhd.h>

## Slide 7: Block device operations
struct block_device_operations is similar to file_operations
Important fields
  /* may need to lock the door for removal media; unlock in the release method; may need to spin the disk up or down */
  int (*open) (struct block_device *dev,
  fmode_t mode);
  int (*release) (struct gendisk *gd,
  fmode_t mode);

## Slide 8: Block device operations
  int (*ioctl) (struct block_dev *bdev,
  fmode_t mode,
  unsigned int cmd,
  unsigned long long arg);
  /* check whether the media has been changed; gendisk represents a disk */
  int (*media_changed) (struct gendisk *gd);
  /* makes new media ready to use */
  int (*revalidate_disk) (struct gendisk *gd);
  struct module *owner; /* = THIS_MODULE */

## Slide 9: Block device operations
Note that no read and write operations
Reads and writes are handled by the request function
  Will be discussed later

## Slide 10: The gendisk structure
struct gendisk represents a disk or a partition
Must initialize the following fields
  int major;
  int first_minor;
  /* need one minor number per partition */
  int minors;
  /* as shown in /proc/partitions & sysfs */
  char disk_name[32];

## Slide 11: The gendisk structure
  struct block_device_operations *fops;
  /* holds I/O requests for this device */
  struct request_queue *queue;
  /* set to GENHD_FL_REMOVABLE for removal media; GENGH_FL_CD for CD-ROMs */
  int flags;
  /* in 512B sectors; use set_capacity() */
  sector_t capacity;

## Slide 12: The gendisk structure
  /* pointer to internal data */
  void *private data;

## Slide 13: The gendisk structure
To allocate, call
  struct gendisk *alloc_disk(int minors);
    minors: number of minor numbers for this disk; cannot be changed later
To deallocate, call
  void del_gendisk(struct gendisk *gd);
To make disk available to the system, call
  void add_disk(struct gendisk *gd);
To make disk unavailable, call
  void put_disk(struct gendisk *gd);

## Slide 14: Initialization in sbull
Allocate a major device number
...
sbull_major = register_blkdev(sbull_major, "sbull");
if (sbull_major <= 0) {
/* error handling */
}
...

## Slide 15: Sbull data structure
struct sbull_dev {
int size; /* Device size in sectors */
u8 *data; /* The data array */
short users; /* How many users */
short media_change; /* Media change? */
spinlock_t lock; /* For mutual exclusion */
struct request_queue *queue; /* The device
request queue */
struct gendisk *gd; /* The gendisk structure */
struct timer_list timer; /* For simulated
media changes */
};
static struct sbull_dev *Devices = NULL;

## Slide 16: Sbull data structure initialization
...
memset (dev, 0, sizeof (struct sbull_dev));
dev->size = nsectors*hardsect_size;
dev->data = vmalloc(dev->size);
if (dev->data == NULL) {
printk(KERN_NOTICE "vmalloc fail\n”);
return;
}
spin_lock_init(&dev->lock);
}
...
/* sbd_request is the request function */
Queue
= dev->queue = blk_init_queue(sbull_request, &dev->lock);
...

## Slide 17: Install the gendisk structure
...
dev->gd = alloc_disk(SBULL_MINORS);
if (! dev->gd) {
printk (KERN_NOTICE "alloc_disk
failure\n");
goto out_vfree;
}
dev->gd->major = sbull_major;
dev->gd->first_minor = which*SBULL_MINORS;
dev->gd->fops = &sbull_ops;
dev->gd->queue = dev->queue;
dev->gd->private_data = dev;
...

## Slide 18: Install the gendisk structure
...
snprintf (dev->gd->disk_name, 32, "sbull%c",
which + 'a');
set_capacity(dev->gd, nsectors * (hardsect_size/KERNEL_SECTOR_SIZE));
add_disk(dev->gd);
...

## Slide 19: Supporting removal media
Check to see if media has been changed, call
int sbull_media_changed(struct gendisk *gd) {
struct sbull_dev *dev = gd->private_data;
return dev->media_change;
}
Prepare the driver for the new media, call
int sbull_revalidate(struct gendisk *gd) {
struct sbull_dev *dev = gd->private_data;
if (dev->media_change) {
dev->media_change = 0;
memset(dev->data, 0, dev->size);
}
return 0;
}

## Slide 20: sbull ioctl
See drivers/block/ioctl.c for built-in commands
To support fdisk and partitions, need to implement a command to provide disk geometry information
  Newer linux versions have a dedicated block device operation called getgeo
  Sbull still has an ioctl call
  Sets number of
    Cylinders
    Heads
    Sectors

## Slide 21: The anatomy of a request
The bio structure
  Contains everything that a block driver needs to carryout out an IO request
  Defined in <linux/bio.h>
Some important fields
  /* the first sector in this transfer */
  sector_t bi_sector;
  /* size of transfer in bytes */
  unsigned int bi_size;

## Slide 22: The anatomy of a request
  /* use bio_data_dir(bio) to check the direction of IOs*/
  unsigned long bi_flags;
  /* number of segments within this bio */
  unsigned short bio_phys_segments;
  struct bio_vec {
  struct page *bv_page;
  unsigned int bv_offset; // within a page
  unsigned int bv_len; // of this transfer
  }

## Slide 23: The bio structure

## Slide 24: The bio structure
For portability, use macros to operate on bio_vec
int segno;
struct bio_vec *bvec;
bio_for_each_segment(bvec, bio, segno) {
// Do something with this segment
}
Current bio_vec entry

## Slide 25: Low-level bio operations
To access the pages directly, use
char *__bio_kmap_atomic(struct bio *bio,
int i,
enum km_type type);
void __bio_kunmap_atomic(char *buffer,
enum km_type type);

## Slide 26: Low-level bio macros
/* returns the page to be transferred next */
struct page *bio_page(struct bio *bio);
/* returns the offset within the current page to be transferred */
int bio_offset(struct bio *bio);
/* returns a kernel logical (shifted) address pointing to the data to be transferred; the address should not be in high memory */
char *bio_data(struct bio *bio);

## Slide 27: The request structure
A request structure is implemented as a linked list of bio structures, with some additional info
Some important fields
  /* first sector that has not been transferred */
  sector_t __sector;
  /* number of sectors yet to transfer */
  unsigned int __data_len;

## Slide 28: The request structure
  /* linked list of bios, access via rq_for_each_bio */
  struct bio *bio;
  /* same as calling bio_data() on current bio */
  char *buffer;

## Slide 29: The request structure
  /* number of segments after merging */
  unsigned short nr_phys_segments;
  struct list_head queuelist;

## Slide 30: The request structure

## Slide 31: Request queues
struct request_queue or request_queue_t
  Include <linux/blkdev.h>
Keep track of pending block IO requests
Create requests with proper parameters
  Maximum size, segments
  Hardware sector size
  Alignment requirement
Allow the use of multiple IO schedulers
  Maximize performance in device-specific ways
    Sort blocks
    Apply deadlines
    Merge adjacent requests

## Slide 32: Queue creation and deletion
To create and initialize a queue, call
request_queue_t
*blk_init_queue(request_fn_proc *request,
spinlock_t *lock);
  request is the request function
  Spinlock controls the access to the queue
  Need to check out-of-memory errors
To deallocate a queue, call
void blk_cleanup_queue(request_queue_t *);

## Slide 33: Queueing functions
Need to hold the queue lock
To get the reference to the next request, call
struct request *blk_fetch_request(request_queue_t *queue);
  Leave the request in the queue
To remove a request from the queue, call
void
blk_dequeue_request(struct request *req);
  Used when a driver operates on multiple requests from a queue concurrently

## Slide 34: Queueing functions
To put a dequeue request back, call
void
blk_requeue_request(request_queue_t *queue,
struct request *req);

## Slide 35: Queue control functions
/* if a device cannot handle more pending requests, call */
void blk_stop_queue(request_queue_t *queue);
/* to restart the queue, call */
void blk_start_queue(request_queue_t *queue);
/* set the highest physical address to which a device can perform DMA; the address can also be BLK_BOUNCE_HIGH, BLK_BOUNCE_ISA, or BLK_BOUNCE_ANY */
void
blk_queue_bounce_limit(request_queue_t *queue,
u64 dma_addr);

## Slide 36: More queue control functions
/* max in sectors */
void
blk_queue_max_sectors(request_queue_t *queue,
unsigned short max);
/* for scatter gather */
void
blk_queue_max_phys_segments(request_queue_t *queue,
unsigned short max);
void
blk_queue_max_hw_segments(request_queue_t *queue,
unsigned short max);
/* in bytes */
void
blk_queue_max_segment_size(request_queue_t *queue,
unsigned int max);

## Slide 37: Request completion functions
After a device has completed transferring the current request chunk, call
bool
__blk_end_request_cur(struct request *req,
int error);
  Indicates that the driver has finished transferring count sectors since the last time.
  Return false if all sectors in this request have been transferred and the request is complete
  Return true if there are still buffers pending

## Slide 38: Request processing
Every device is associated with a queue
To read or write a block device, call
void request(request_queue_t *queue);
  Runs in an atomic context
    Cannot access the current process
  May return before completing the request

## Slide 39: Working with sbull bios
static void sbull_request(struct request_queue *q)
{
struct request *req;
while ((req = blk_fetch_request(q)) != NULL) {
struct sbull_dev *dev = req->rq_disk->private_data;
sbull_transfer(dev, blk_rq_pos(req), blk_rq_cur_sectors(req), req->buffer, rq_data_dir(req));
__blk_end_request_cur(req, 0);
}
}

## Slide 40: sbull_transfer
static void sbull_transfer(struct sbull_dev *dev, unsigned
long sector, unsigned long nsect,
char *buffer, int write)
{
unsigned long offset = sector*KERNEL_SECTOR_SIZE;
unsigned long nbytes = nsect*KERNEL_SECTOR_SIZE;
if ((offset + nbytes) > dev->size) {
printk (KERN_NOTICE "Beyond-end write (%ld %ld)\n",
offset, nbytes);
return;
}
if (write)
memcpy(dev->data + offset, buffer, nbytes);
else
memcpy(buffer, dev->data + offset, nbytes);
}

## Slide 41: Block devices
After character devices and network devices, block devices are another important device type of any system
Used for the storage of application code and data, and user data, they are often critical to the overall performance of the system
A dedicated subsystem, the block layer is in charge of managing the block devices, together with hardware specific device drivers
This subsystem has been completely rewritten during the 2.5 development cycle. The API covered in these slides is the one found in 2.6.x kernels.

## Slide 42: From userspace
From userspace, block devices are accessed using device files, usually stored in /dev/
  Created manually or dynamically by udev
Most of the time, they store filesystems : they are not accessed directly, but rather mounted, so that the contents of the filesystem appears in the global hierarchy of files
Block devices are also visible through the sysfs filesystem, in the /sys/block/ directory
$ ls /sys/block/
dm-0 dm-2 loop0 loop2 ram0 ram2 ram4 ram6 sda
dm-1 dm-3 loop1 loop3 ram1 ram3 ram5 ram7

## Slide 43: Global architecture
Virtual File System
Individual filesystems
(ext3, vfat, etc.)
Buffer/page cache
Block layer
User application
User application
Kernel
User

## Slide 44: Global architecture (2)
An user application can use a block device
  Through a filesystem, by reading, writing or mapping files
  Directly, by reading, writing or mapping a device file representing a block device in /dev
In both cases, the VFS subsystem in the kernel is the entry point for all accesses
  A filesystem driver is involved if a normal file is being accessed
The buffer/page cache of the kernel stores recently read and written portions of block devices
  It is a critical component for the performance of the system

## Slide 45: Inside the block layer
Buffer/page cache
Block layer
Hardware
Block
driver
I/O scheduler
Block
driver
Block
driver
Block
driver
Block
driver

## Slide 46: Inside the block layer (2)
The block layer allows block device drivers to receive I/O requests, and is in charge of I/O scheduling
I/O scheduling allows to
  Merge requests so that they are of greater size
  Re-order requests so that the disk head movement is as optimized as possible
Several I/O schedulers with different policies are available in Linux.
A block device driver can handle the requests before or after they go through the I/O scheduler

## Slide 47: Two main types of drivers
Most of the block device drivers are implemented below the I/O scheduler, to take advantage of the I/O scheduling
  Hard disk drivers, CD-ROM drivers, etc.
For some drivers however, it doesn't make sense to use the IO scheduler
  RAID and volume manager, like md
  The special loop driver
  Memory-based block devices

## Slide 48: Available I/O schedulers
Four I/O schedulers in current kernels
  Noop, for non-disk based block devices
  Anticipatory, tries to anticipate what could be the next accesses
  Deadline, tries to guarantee that an I/O will be served within a deadline
  CFQ, the Complete Fairness Queuing, the default scheduler, tries to guarantee fairness between users of a block device
The current scheduler for a device can be get and set in /sys/block/<dev>/queue/scheduler

## Slide 49: Kernel options
CONFIG_BLOCK
  Allows to selectively enable or disable the block layer. A kernel without the block layer can be useful if using MTD devices, storage over the network, or a filesystem in initramfs
  Only available if CONFIG_EMBEDDED is set
CONFIG_IOSCHED_NOOP, CONFIG_IOSCHED_AS, CONFIG_IOSCHED_DEADLINE, CONFIG_IOSCHED_CFQ
  Allows to enable or disable different I/O schedulers. They can be compiled as module, loaded and changed dynamically, on a per-device basis.

## Slide 50: Looking at the code
The block device layer is implemented in the block/ directory of the kernel source tree
  This directory also contains the I/O scheduler code, in the *-iosched.c files.
A few simple block device drivers are implemented in drivers/block/, including
  loop.c, the loop driver that allows to see a regular file as a block device
  brd.c, a ramdisk driver
  nbd.c, a network-based block device driver

## Slide 51: Implementing a block device driver
A block device driver must implement a set of operations to be registered in the block layer and receive requests from the kernel
A block device driver can directly implement this set of operation. However, as in many areas in the kernel, subsystems have been created to factorize common code of drivers for devices of the same type
  SCSI devices
  PATA/SATA devices
  MMC/SD devices
  etc.

## Slide 52: Implementing a block device driver (2)
Generic block layer
Block
driver
SCSI
subsystem
SCSI
driver
libata
subsystem
PATA/SATA
driver
IDE
subsystem
IDE
driver
MMC
subsystem
MMC/SD
driver
usb
storage

## Slide 53: Registering the major
The first step in the initialization of a block device driver is the registration of the major number
  int register_blkdev(unsigned int major, const char *name);
  Major can be 0, in which case it is dynamically allocated
  Once registered, the driver appears in /proc/devices with the other block device drivers
Of course, at cleanup time, the major must be unregistered
  void unregister_blkdev(unsigned int major, const char *name);
The prototypes of these functions are in <linux/fs.h>

## Slide 54: struct gendisk
The structure representing a single block device, defined in <linux/genhd.h>
  int major, major of the device driver
  int first_minor, minor of this device. A block device can have several minors when it is partitionned
  int minors, number of minors. 1 for non-partitionable devices
  struct block_device_operations *fops, pointer to the list of block device operations
  struct request_queue *queue, the queue of requests
  sector_t capacity, size of the block device in sectors

## Slide 55: Initializing a disk
Allocate a gendisk structure struct gendisk *alloc_disk(int minors) minors tells the number of minors to be allocated for this disk. Usually 1, unless your device can be partitionned
Allocate a request queue struct request_queue *blk_init_queue (request_fn_proc *rfn, spinlock_t *lock) rfn is the request function (covered later). lock is a optional spinlock needed to protect the request queue against concurrent access. If NULL, a default spinlock is used

## Slide 56: Initializing a disk (2)
Initialize the gendisk structure Fields major, first_minor, fops, disk_name and queue should at the minimum be initialized private_data can be used to store a pointer to some private information for the disk
Set the capacity void set_capacity(struct gendisk *disk, sector_t size) The size is a number of 512-bytes sectors. sector_t is 64 bits wide on 64 bits architectures, 32 bits on 32 bits architecture, unless CONFIG_LBD (large block devices) has been selected

## Slide 57: Initializing a disk (3)
Add the disk to the system void add_disk(struct gendisk *disk); The block device can now be accessed by the system, so the driver must be fully ready to handle I/O requests before calling add_disk(). I/O requests can even take place during the call to add_disk().

## Slide 58: Unregistering a disk
Unregister the disk void del_gendisk(struct gendisk *gp);
Free the request queue void blk_cleanup_queue(struct request_queue *);
Drop the reference taken in alloc_disk() void put_disk(struct gendisk *disk);

## Slide 59: block_device_operations
A set of function pointers
  open() and release(), called when a device handled by the driver is opened and closed
  ioctl() for driver specific operations. unlocked_ioctl() is the non-BKL variant, and compat_ioctl() for 32 bits processes running on a 64 bits kernel
  direct_access() required for XIP support, see http://lwn.net/Articles/135472/
  media_changed() and revalidate() required for removable media support
  getgeo(), to provide geometry informations to userspace

## Slide 60: A simple request() function
static void foo_request(struct request_queue *q)
{
struct request *req;
while ((req = elv_next_request(q)) != NULL) {
if (! blk_fs_request(req)) {
__blk_end_request(req, 1, req->nr_sectors << 9);
continue;
}
/* Do the transfer here */
__blk_end_request(req, 0, req->nr_sectors << 9);
}
}

## Slide 61: A simple request() function (2)
Information about the transfer are available in the struct request
  sector, the position in the device at which the transfer should be made
  current_nr_sectors, the number of sectors to transfer
  buffer, the location in memory where the data should be read or written to
  rq_data_dir(), the type of transfer, either READ or WRITE
__blk_end_request() or blk_end_request() is used to notify the completion of a request. __blk_end_request() must be used when the queue lock is already held

## Slide 62: Data structures in a nutshell
major
first_minor
minors
disk_name
fops
queue
private_data
capacity
...
gendisk
open()
release()
ioctl()
media_changed()
revalidate()
getgeo()
...
block_device_operations
request_fn
List of requests
...
request_queue
sector
current_nr_sectors
buffer
rq_disk
q
...
request
...
foo_device

## Slide 63: Request queue configuration (1)
blk_queue_bounce_limit(queue, u64) Tells the kernel the highest physical address that the device can handle. Above that address, bouncing will be made. BLK_BOUNCE_HIGH, BLK_BOUNCE_ISA and BLK_BOUNCE_ANY are special values
  HIGH: will bounce if the pages are in high-memory
  ISA: will bounce if the pages are not in the ISA 16 Mb zone
  ANY: will not bounce

## Slide 64: Request queue configuration (2)
blk_queue_max_sectors(queue, unsigned int) Tell the kernel the maximum number of 512 bytes sectors for each request.
blk_queue_max_phys_segments(queue, unsigned short) blk_queue_max_hw_segments(queue, unsigned short) Tell the kernel the maximum number of non-memory-adjacent segments that the driver can handle in a single request (default 128).
blk_queue_max_segment_size(queue, unsigned int) Tell the kernel how large a single request segment can be

## Slide 65: Request queue configuration (3)
blk_queue_segment_boundary(queue, unsigned long mask) Tell the kernel about memory boundaries that your device cannot handle inside a given buffer. By default, no boundary.
blk_queue_dma_alignement(queue, int mask) Tell the kernel about memory alignment constraints of your device. By default, 512 bytes alignment.
blk_queue_hardsect_size(queue, unsigned short max) Tell the kernel about the sector size of your device. The requests will be aligned and a multiple of this size, but the communication is still in number of 512 bytes sectors.

## Slide 66: Inside a request
A request is composed of several segments, that are contiguous on the block device, but not necessarily contiguous in physical memory
A struct request is in fact a list of struct bio
A bio is the descriptor of an I/O request submitted to the block layer. bios are merged together in a struct request by the I/O scheduler.
As a bio might represent several pages of data, it is composed of several struct bio_vec, each of them representing a page of memory

## Slide 67: Inside a request (2)
bio
sector
nr_sectors
q
rq_disk
...
request
bi_sector
bi_next
bi_bdev
bi_size
bi_vcnt
bi_io_vec
bio
bi_sector
bi_next
bi_bdev
bi_size
bi_vcnt
bi_io_vec
bio
bv_page
bv_len
bv_offset
bio_vec
bv_page
bv_len
bv_offset
bio_vec
bv_page
bv_len
bv_offset
bio_vec
bv_page
bv_len
bv_offset
bio_vec

## Slide 68: Request example
Block device
32 sect
1024
Memory
bio
sector=1024
nr_sectors=32
request
bi_sector=1024
bi_next
bi_size=8192
bi_vcnt=2
bi_io_vec
bio
bi_sector=1040
bi_next
bi_size=8192
bi_vcnt=2
bi_io_vec
bio
bv_len
bv_offset
bv_page
4096
0
4096
0
bv_len
bv_offset
bv_page
4096
0
4096
0
bio
vec
[2]
bio
vec
[2]

## Slide 69: Asynchronous operations
If you handle several requests at the same time, which is often the case when handling them in asynchronous manner, you must dequeue the requests from the queue : void blkdev_dequeue_request(struct request *req);
If needed, you can also put a request back in the queue : void elv_requeue_request(struct request_queue *queue, struct request *req);

## Slide 70: Asynchronous operations (2)
Once the request is outside the queue, it's the responsibility of the driver to process all segments of the request
Either by looping until blk_end_request() returns 0
Or by using the rq_for_each_segment() macro
struct bio_vec *bvec;
struct req_iterator iter;
rq_for_each_segment(bvec, rq, iter)
{
/* rq->sector contains the current sector
page_address(bvec->bv_page) + bvec->bv_offset points to the data
bvec->bv_len is the length */
rq->sector += bvec->bv_len / KERNEL_SECTOR_SIZE;
}
blk_end_request(rq, 0, rq->nr_sectors << 9);

## Slide 71: DMA
The block layer provides an helper function to « convert » a request to a scatter-gather list : int blk_rq_map_sg(struct request_queue *q, struct request *rq, struct scatterlist *sglist)
sglist must be a pointer to an array of struct scatterlist, with enough entries to hold the maximum number of segments in a request. This number is specified at queue initialization using blk_queue_max_hw_segments().
The function returns the actual number of scatter gather list entries filled.

## Slide 72: DMA (2)
Once the scatterlist is generated, individual segments must be mapped at addresses suitable for DMA, using : int dma_map_sg(struct device *dev, struct scatterlist *sglist, int count, enum dma_data_direction dir);
dev is the device on which the DMA transfer will be made
dir is the direction of the transfer (DMA_TO_DEVICE, DMA_FROM_DEVICE, DMA_BIDIRECTIONAL)
The addresses and length of each segment can be found using sg_dma_addr() and sg_dma_len() on scatterlist entries.

## Slide 73: DMA (3)
After the DMA transfer completion, the segments must be unmapped, using int dma_unmap_sg(struct device *dev, struct scatterlist *sglist, int hwcount, enum dma_data_direction dir)

## Slide 74: MMC / SD
MMC Core
CONFIG_MMC
drivers/mmc/core/
MMC Host Driver
CONFIG_MMC_...
drivers/mmc/host/...
Block layer
MMC block device driver
CONFIG_MMC_BLOCK
drivers/mmc/card/{block,queue}.c

## Slide 75: MMC host driver
For each host
  struct mmc_host *mmc_alloc_host(int extra, struct device *dev)
  Initialize struct mmc_host fields: caps, ops, max_phys_segs, max_hw_segs, max_blk_size, max_blk_count, max_req_size
  int mmc_add_host(struct mmc_host *host)
At unregistration
  void mmc_remove_host(struct mmc_host *host)
  void mmc_free_host(struct mmc_host *host)

## Slide 76: MMC host driver (2)
The mmc_host->ops field points to a mmc_host_ops structure
  Handle an I/O request void (*request)(struct mmc_host *host, struct mmc_request *req);
  Set configuration settings void (*set_ios)(struct mmc_host *host, struct mmc_ios *ios);
  Get read-only status int (*get_ro)(struct mmc_host *host);
  Get the card presence status int (*get_cd)(struct mmc_host *host);