## Slide 1: DEVICE DRIVERS
Day 35
Linux Device Driver Training
Presented by,
Ganavi M
Ganavigowda512@gmail.com

## Slide 2: A “real” network driver?
We want to construct a Linux network device-driver that is able to send and receive packets

## Slide 3: Our ‘framework.c’ demo
Earlier in our course we wrote a ‘skeleton’ network device-driver that showed us the minimum elements necessary to interact successfully with the Linux kernel, though it did not program any actual hardware
Since then we have learned how to write code that does control network hardware, by building ‘character-mode’ Linux drivers

## Slide 4
Role of device-drivers
hardware devices
network
device driver
Linux
operating system
kernel
networking
subsystem
application
program
standard
runtime
libraries
user space kernel space
file
subsystem
character
device driver

## Slide 5: Pedagogy
Using character-mode device-drivers has advantages for studying how the network controller hardware works -- because we don’t have to worry about interfacing with the Linux kernel’s networking subsystem
But we don’t end up with a ‘real’ network device-driver until we do create code that can work with that networking subsystem

## Slide 6
Source-code layout
#include <linux/module.h>
#include <linux/etherdevice.h>
…
typedef struct {
/* driver’s private data */
} MY_DRIVERDATA;
char modname[ ] = “netframe”;
struct net_device *netdev;
netframe.c
my_init
my_exit
The mandatory module-
administration functions
my_open()
my_stop()
my_hard_start_xmit()
my_isr()
my_get_info()
The network driver’s
“payload” functions
Optional pseudo-file (for
debugging assistance)

## Slide 7: ‘minimal’ functionality
Use the mimimum number of descriptors
Use simple ‘legacy’ descriptor-formats
Maintain a minimal set of driver statistics
Omit flow-control and VLAN tagging
Omit nonessential interrupt-processing
Omit use of packet-filtering options
Omit use of device’s ‘offload’ options

## Slide 8: Interactions with the kernel
module_init() calls ‘register_netdev()’
module_exit() calls ‘unregister_netdev()’
open() calls ‘netif_start_queue()’
stop() calls ‘netif_stop_queue()’
hard_start_xmit() calls ‘dev_kfree_skb()’
rx_handler() calls ‘dev_alloc_skb()’ and netif_rx()’

## Slide 9: ‘mynetdvr.c’
We can demonstrate the basic transmit and receive functionality of our network driver using a pair of ‘anchor’ machines
But we have to work around some slight amount of interference with the already-installed ‘e1000’ network-driver which is supporting our ability to do remote login via the ‘eth0’ device interface

## Slide 10: The ‘anchor’ installation-steps
1. Bring down the ‘eth1’ interface
    $ sudo /sbin/ifconfig eth1 down
2. Install our network device-driver
    $ /sbin/insmod mynetdvr.ko
3. Bring down the ‘eth1’ interface again
    $ sudo /sbin/ifconfig eth1 down
4. Assign IP-address to the ‘eth2’ interface
    $ sudo /sbin/ifconfig eth2 192.168.2.x

## Slide 11: Demo #1: ‘ping’
Suppose you assigned the following pair of IP-addresses to the ‘eth2’ interface on ‘anchor01’ and the ‘anchor02’ machines, respectively:
    anchor01$ sudo /sbin/ifconfig eth2 192.168.2.101
    anchor02$ sudo /sbin/ifconfig eth2 192.168.2.102
Then try to ‘ping’ anchor02 from anchor01:
    anchor01$ ping 192.168.2.102

## Slide 12: Demo #2: client-server
You can try executing our ‘udpserver’ and ‘udpclient’ application-programs:
  First execute ‘udpserver’ on anchor01
    anchor01$ udpserver
    Socket has port #32774
  Then execute ‘udpclient’ on anchor02
    anchor02$ udpclient 192.168.2.101 32774

## Slide 13: Demo #3: ‘nicwatch’
Remember, you can watch the incoming and outgoing packets on an interface by using our ‘nicwatch’ application:
    anchor01$ nicwatch eth2
    anchor02$ nicwatch eth2

## Slide 14: Chapter - Networking and Internetworking

## Slide 15
Introduction

## Slide 16: Building Blocks
Nodes: PC, special-purpose hardware…
  hosts
  switches
Links: coax cable, optical fiber…
  point-to-point
  multiple access
■ ■ ■
(a)
(b)

## Slide 17: Switched Networks
  two or more nodes connected by a link, or
  two or more networks connected by a node
A network can be defined recursively as...

## Slide 18: Simplified view of the QMW Computer Science network (in mid-2000)
file
compute
dialup
hammer
henry
hotpoint
138.37.88.230
138.37.88.162
bruno
138.37.88.249
router/
sickle
138.37.95.241
138.37.95.240/29
138.37.95.249
copper
138.37.88.248
firewall
web
138.37.95.248/29
server
desktop computers
138.37.88.xx
subnet
subnet
Eswitch
138.37.88
server
server
server
138.37.88.251
custard
138.37.94.246
desktop computers
Eswitch
138.37.94
hub
hub
Student subnet
Staff subnet
other
servers
router/
firewall
138.37.94.251
%
1000 Mbps Ethernet
Eswitch: Ethernet switch
100 Mbps Ethernet
file server/
gateway
printers
Campus
router
Campus
router
138.37.94.xx

## Slide 19: Firewall configurations

## Slide 20: Addressing and Routing
Address: byte-string that identifies a node
  usually unique
Routing: process of forwarding messages to the destination node based on its address
Types of addresses
  unicast: node-specific
  broadcast: all nodes on the network
  multicast: some subset of nodes on the network

## Slide 21: Inter-Process Communication
Turn host-to-host connectivity into process-to-process communication.
Fill gap between what applications expect and what the underlying technology provides.

## Slide 22: Multiplexing
Circuit switching: carry bit streams
  original telephone network
Packet switching: store-and-forward messages
  Internet

## Slide 23: Statistical Multiplexing
On-demand time-division
Schedule link on a per-packet basis
Packets from different sources interleaved on link
Buffer packets that are contending for the link
Buffer (queue) overflow is called congestion
■ ■ ■

## Slide 24: What Goes Wrong in the Network?
Bit-level errors (electrical interference)
Packet-level errors (congestion)
Link and node failures
Packets are delayed
Packets are deliver out-of-order
Third parties eavesdrop

## Slide 25: Conceptual layering of protocol software
Layer n
Layer 2
Layer 1
Message sent
Message received
Communication
medium
Sender
Recipient

## Slide 26: Protocol layers in the ISO Open Systems Interconnection (OSI) model
most peer-to-peer communication is indirect
peer-to-peer is direct only at hardware level

## Slide 27: Encapsulation as it is applied in layered protocols

## Slide 28: ISO Architecture

## Slide 29: OSI protocol summary
Layer
Description
Examples
Application
Protocols that are designed to meet the communication requirements of
specific applications, often defining the interface to a service.
HTTP,
FTP
,
SMTP,
CORBA IIOP
Presentation
Protocols at this level transmit data in a network representation that is
independent of the representations used in individual computers, which may
differ. Encryption is also performed in this layer, if required.
Secure Sockets
(
SSL),CORBA Data
Rep.
Session
At this level reliability and adaptation are performed, such as detection of
failures and automatic recovery.
Transport
This is the lowest level at which messages (rather than packets) are handled.
Messages are addressed to communication ports attached to processes,
Protocols in this layer may be connection-oriented or connectionless.
TCP,
UDP
Network
Transfers data packets between computers in a specific network. In a WAN
or an internetwork this involves the generation of a route passing through
routers. In a single LAN no routing is required.
IP,
ATM virtual
circuits
Data link
Responsible for transmission of packets between nodes that are directly
connected by a physical link. In a WAN transmission is between pairs of
routers or between routers and hosts. In a LAN it is between any pair of hosts.
Ethernet MAC,
ATM cell transfer,
PPP
Physical
The circuits and hardware that drive the network. It transmits sequences of
binary data by analogue signalling, using amplitude or frequency modulation
of electrical signals (on cable circuits), light signals (on fibre optic circuits)
or other electromagnetic signals (on radio and microwave circuits).
Ethernet base- band
signalling,
ISDN

## Slide 30: TCP/IP layers
Messages (UDP) or Streams (TCP)
Application
Transport
Internet
UDP or TCP packets
IP datagrams
Network-specific frames
Message
Layers
Underlying network
Network interface

## Slide 31: Encapsulation in a message transmitted via TCP over an Ethernet
Application message
TCP header
IP header
Ethernet header
Ethernet frame
port
TCP
IP

## Slide 32: The programmer's conceptual view of a TCP/IP Internet

## Slide 33: Internet Architecture
Hourglass Design
Application vs Application Protocol (FTP, HTTP)
■ ■ ■
FTP
TCP
UDP
IP
NET
1
NET
2
NET
n
HTTP
SMTP
TFTP

## Slide 34: Protocol Multiplexing
Multiplexing and Demultiplexing (demux key)
Encapsulation (header/body)
Host
Host
Application
program
Application
program
RRP
Data
Data
HHP
RRP
HHP
Application
program
Application
program
RRP Data
RRP Data
HHP RRP Data

## Slide 35
Switching

## Slide 36: Scalable Networks
Switch
  Connect links to form a larger network.
  Connect switches to form a larger network.
  forwards packets from input port to output port
  port selected based on address in packet header
Advantages
  store and forward
  support large numbers of hosts

## Slide 37: Datagram Switching
No connection setup phase
  Sometimes called connectionless model
Each packet forwarded independently
Each switch maintains a forwarding (routing) table
  Eg. Switch 1

## Slide 38: Datagram Model
Source host has no way of knowing if the network is capable of delivering a packet or if the destination host is even up.
  No QoS
Since packets are treated independently, it is possible to route around link and node failures.
Since every packet must carry the full address of the destination, the overhead per packet is higher than for the connection-oriented model.

## Slide 39: Learning Bridges
Do not forward to all the other ports (broadcast) when unnecessary
Maintain forwarding table
Host Port
A 1
B 1
C 1
X 2
Y 2
Z 2
Learn table entries based on source address
Table is an optimization; need not be complete
Always forward broadcast frames

## Slide 40
Routing (IP)

## Slide 41: Internetworking
Concatenation of Different Networks

## Slide 42: IP Internet
Connecting Problem 1: Heterogeneity of Networks
  Solution: Layered Protocol Stack (IP over …… )
Problem 2: Scalability in Routing and Addressing
  Solution: Address Hierarchy

## Slide 43: Service Model
Connectionless (datagram-based)
Best-effort delivery (unreliable service)
  packets can be lost, delayed, duplicated, delivered out of order.
Datagram format: IP header

## Slide 44: IP Header
Version (always set to the value 4 for IP v4)
IP Header Length (number of 32 -bit words forming the header, usually five)
Size of Datagram (in bytes, header + data)
Flags 3 bits: R (reserved bit set to 0) DF (Don't fragment ) MF (More fragments)
Time To Live (Number of hops /links which the packet may be routed over, decremented by most routers - used to prevent accidental routing loops)
Protocol (the type of transport packet being carried (e.g. 1 = ICMP; 6 = TCP; 17= UDP).
Header Checksum (A 1's complement checksum of IP header, updated whenever the packet header is modified by a node. Packets with an invalid checksum are discarded by all nodes in an IP network)
Source Address / Destination Address

## Slide 45: Internet address structure, showing field sizes in bits
globally unique
hierarchical: network + host

## Slide 46: Decimal representation of Internet addresses
octet 1
octet 2
octet 3
Class A:
1 to 127
0 to 255
0 to 255
1 to 254
Class B:
128 to 191
Class C:
192 to 223
224 to 239
Class D (multicast):
Network ID
Network ID
Network ID
Host ID
Host ID
Host ID
Multicast address
0 to 255
0 to 255
1 to 254
0 to 255
0 to 255
0 to 255
0 to 255
0 to 255
0 to 255
Multicast address
0 to 255
0 to 255
1 to 254
240 to 255
Class E (reserved):
1.0.0.0 to
127.255.255.255
128.0.0.0 to
191.255.255.255
192.0.0.0 to
223.255.255.255
224.0.0.0 to
239.255.255.255
240.0.0.0 to
255.255.255.255
Range of addresses

## Slide 47: Datagram Forwarding Strategy
Every datagram contains destination’s address
if connected to destination network, then forward to the host in LAN
  If network number of destination IP == my network number
if not directly connected, then forward to the host’s default router
Each router maintains a forwarding table
  forwarding table maps network number (rather than host address) into next hop or interface number (if directly connected)

## Slide 48
  Traffic: H1 → H3, H1 → H8
  R1: default router is R2
  R2 Routing Table:
  Network Number Next Hop Interface
1 R3 interface 1
2 R1 interface 0
3 - interface 1
4 - interface 0

## Slide 49: Address Translation in LAN
Map IP addresses into physical addresses of the destination host (if connected directly) or the next hop router
ARP
  Each host caches its table of IP to physical address bindings
  table entries are discarded if not refreshed
    timeout in about 10 minutes
  broadcast request if IP address not in table
  target machine send its physical address to the sender
  target machine also updates add entry of the source in its table
    It is likely that the target will send IP packets to the source later on.
  Other hosts (who receives the broadcasted request) update table if already have an entry

## Slide 50: End-to-End Protocols
Underlying best-effort network
  drop messages
  re-orders messages
  delivers duplicate copies of a given message
  limits packet (not message) to some finite size
  delivers messages after an arbitrarily long delay
Common end-to-end services
  guarantee message delivery
  deliver messages in the same order they are sent
  deliver at most one copy of each message
  support arbitrarily large messages
  support synchronization between sender and receiver
  allow the receiver to flow control the sender
  support multiple application processes on each host

## Slide 51
End-to-End Protocols
(UDP/TCP)

## Slide 52: Simple Demultiplexor (UDP)
Unreliable and unordered datagram service
Adds multiplexing
No flow control or error control
  no need for sender-side buffer)
Endpoints identified by ports
  servers listens at well-known ports!
  see /etc/services on Unix
Header format
Optional checksum
  psuedo header (IP.src, IP.dsest, IP.proto, UDP.len) + UDP header + data

## Slide 53: TCP Overview
Connection-oriented
Byte-stream
  app writes bytes
  TCP sends segments
  app reads bytes
Full duplex
Flow control: keep sender from overrunning receiver
Congestion control: keep sender from overrunning network
Application process
Write
bytes
TCP
Send buffer
Segment
Segment
Segment
Transmit segments
Application process
Read
bytes
TCP
Receive buffer
■ ■ ■

## Slide 54: Segment Format

## Slide 55: Segment Format (cont)
Each connection identified with 4-tuple:
  (SrcPort, SrcIPAddr, DsrPort, DstIPAddr)
Sliding window + flow control
  acknowledgment, SequenceNum, AdvertisedWinow
Flags
  SYN, FIN, RESET, PUSH, URG, ACK
Checksum
  pseudo header + TCP header + data

## Slide 56: Connection Establishment and Three-Way Handshake
Active participant
(client)
Passive participant
(server)
SYN, SequenceNum =
x
ACK, Acknowledgment =y+1
Acknowledgment =x+1
SYN+ACK, SequenceNum=y,

## Slide 57: Reliability and Flow Control
The receiver’s buffer has two purposes
  Reorder segments received out of order
  Hold data unread by the application
The sender cannot send more than AdvertisedWindow bytes of unacknowledged data at any given time (Flow Control).
The sender retransmits after timeout
  Adaptive RTT measurement.

## Slide 58: Socket API
Creating a socket
  int socket(int domain, int type, int protocol)
    type = SOCK_STREAM, SOCK_DGRAM, SOCK_RAW
Passive Open (on server)
  int bind(int socket, struct sockaddr *addr, int addr_len)
  int listen(int socket, int backlog)
  int accept(int socket, struct sockaddr *addr, int addr_len)
Active Open (on client)
  int connect(int socket, struct sockaddr *addr,
  int addr_len)
Sending/Receiving Messages
  int send(int socket, char *msg, int mlen, int flags)
  int recv(int socket, char *buf, int blen, int flags)

## Slide 59
Wireless LAN

## Slide 60: Ethernet Overview
The most successful Local Area Networks
Bandwidth: 10Mbps, 100Mbps (Fast), 1Gbps
Avoid Simultaneous on a Shared Line: CSMA/CD
  multiple access
  carrier sense:
    listen before transmitting.
    distinguish an idle and busy link.
  collision detection
    listen while transmitting.
    Collision: What you hear is different from what you listen

## Slide 61: Ethernet Frame
Frame Format
Addresses
  unique, 48-bit unicast address assigned to each adapter
    example: 8:0:e4:b1:2
  Every body hears the frame (shared media). But the one with matching destination address picks up.
  broadcast: all 1s
  multicast: first bit is 1. The host can configure its adaptor to accept some multicast addresses
Preamble (a seq. alternating 0s and 1s ) indicates the start of a frame
Type: high-level protocols

## Slide 62: Transmit Algorithm
If line is idle…
  send immediately
  upper bound message size of 1500 bytes
    Limited occupancy on the line.
  must wait 9.6us between back-to-back frames
    To allow other hosts to send.
If line is busy…
  wait until idle and transmit immediately

## Slide 63: Collisions
The remote side may send its frame before it hears the frame currently being sent
  Both sides detect an idle line
  Due to the propagation delay
For A to detect the collision
  Collisions can only be detected during transmission
  51.2us •10Mbps = 64 bytes

## Slide 64: Upon Collision
Send 32 jam bits, then stop transmitting frame
  To ensure other hosts to detect conllision
minimum frame is 64 bytes (header + 46 bytes of data)
delay and try again: exponential backoff
  1st time: 0 or 51.2us selected at random
  2nd time: 0, 51.2, or 102.4us
  nth time: k x 51.2us, for randomly selected k=0..2n - 1
  give up after several tries (usually 16)

## Slide 65: Wireless LANs
IEEE 802.11
Bandwidth: 1 - 11 Mbps
Physical Media
  diffused infrared (10m)
    Diffused: the sender do not need a clear line of sight.
  spread spectrum radio (2.4GHz): 11 Mbps  54Mbps

## Slide 66: Wireless LAN configuration

## Slide 67: Infrastructure mode
mobile terminal
access point
fixed
terminal
application
TCP
802.11 PHY
802.11 MAC
IP
802.3 MAC
802.3 PHY
application
TCP
802.3 PHY
802.3 MAC
IP
802.11 MAC
802.11 PHY
LLC
infrastructure
network
LLC
LLC

## Slide 68: Supporting Mobility
Case 1: ad hoc networking
Case 2: access points (AP)
  Tethered
  each mobile node associates with an AP (base station)
  Mobile nodes sends to AP first; AP forwards

## Slide 69: Collisions Avoidance
Similar to Ethernet: Wait until link idle
Problem: hidden and exposed nodes
  A  C; C  B;
    Collides at B
    A, C cannot detect: hidden nodes
  B  A; C  D;
    C assumes collision
    Actually no collision at A or D
Cannot (listen) detect collision when transmit

## Slide 70: 802.11 MAC
Priorities
  defined through different inter frame spaces
  no guaranteed, hard priorities
  SIFS (Short Inter Frame Spacing)
    highest priority, for ACK, CTS, polling response
  PIFS (PCF IFS)
    medium priority, for time-bounded service using PCF
  DIFS (DCF, Distributed Coordination Function IFS)
    lowest priority, for asynchronous data service
t
medium busy
SIFS
PIFS
DIFS
DIFS
next frame
contention
direct access if medium is free  DIFS

## Slide 71: 802.11 CSMA/CA
t
medium busy
DIFS
DIFS
next frame
contention window
(randomized back-off mechanism)
  station ready to send starts sensing the medium (Carrier Sense based on CCA, Clear Channel Assessment)
  if the medium is free for the duration of an Inter-Frame Space (IFS), the station can start sending (IFS depends on service type)
  if the medium is busy, the station has to wait for a free IFS, then the station must additionally wait a random back-off time (collision avoidance, multiple of slot-time)
  if another station occupies the medium during the back-off time of the station, the back-off timer stops (fairness)
slot time
direct access if medium is free  DIFS

## Slide 72: 802.11 CSMA/CA: contention resolution
t
busy
boe
station1
station2
station3
station4
station5
packet arrival at MAC
DIFS
boe
boe
boe
busy
elapsed backoff time
bor
residual backoff time
busy
medium not idle (frame, ack etc.)
bor
bor
DIFS
boe
boe
boe
bor
DIFS
busy
busy
DIFS
boe
busy
boe
boe
bor
bor

## Slide 73: 802.11 CSMA/CA: detailed
Sending unicast packets
  station has to wait for DIFS before sending data
  receivers acknowledge at once (after waiting for SIFS) if the packet was received correctly (CRC)
  automatic retransmission of data packets in case of transmission errors
t
SIFS
DIFS
data
ACK
waiting time
other
stations
receiver
sender
data
DIFS
contention

## Slide 74: Multiple Access with Collision Avoidance (MACA)
Sender transmits RequestToSend (RTS) frame
  Specifying how long to hold the medium
Receiver replies with ClearToSend (CTS) frame
Neighbors…
  see CTS: keep quiet
  see RTS but not CTS: receiver cannot hear me, ok to transmit
Receive sends ACK when has frame
  neighbors silent until see ACK
Collisions
  no collisions detection
  known when don’t receive CTS or ACK
    The cost of collision with RTS/CTS is much smaller
  exponential backoff

## Slide 75: 802.11: RTS & CTS
Sending unicast packets
  station can send RTS with reservation parameter after waiting for DIFS (reservation determines amount of time the data packet needs the medium)
  acknowledgement via CTS after SIFS by receiver (if ready to receive)
  sender can now send data at once, acknowledgement via ACK
  other stations store medium reservations distributed via RTS and CTS
t
SIFS
DIFS
data
ACK
defer access
other
stations
receiver
sender
data
DIFS
contention
RTS
CTS
SIFS
SIFS
NAV (RTS)
NAV (CTS)

## Slide 76: Mobility (cont)
Scanning (selecting an AP)
  node sends Probe frame
  all AP’s w/in reach reply with ProbeResponse frame
  node selects one AP; sends it AssociateRequest frame
  AP replies with AssociationResponse frame
When
  active: when join or move
    Signal with old AP weakened
    new AP informs old AP via tethered network
  passive: AP periodically sends Beacon frame